ESP32 16mm Projector Pinout

Breadboard row numbers

Breadboard row numbers

1					Encoder 3.3V		1
2	Blue	NeoPixel	Jumper to GPIO 15					Motor 6V BEC		red	2
3	Red	UI 3.3V		3.3V	1		38	GND	Motor GND		brown	3
4				EN	2		37	GPIO23		Encoder SPI MOSI	White	4
5	White	Pot: Shutter Angle		GPIO36	3		36	GPIO22	Motor PWM OUT		Orange	5
6	Grey	Pot: Shutter Blades		GPIO39	4		35	X				6
7	Purple	Pot: Lamp Slewing		GPIO34	5		34	X				7
8	Blue	Pot: Lamp Bright		GPIO35	6		33	GPIO21	Motor ESC PGM		Yellow	8
9	Green	Pot: Motor Slewing		GPIO32	7		32	GND		Encoder GND	Black	9
10	Yellow	Pot: Motor Speed		GPIO33	8		31	GPIO19		Encoder SPI MISO	Grey	10
11	Orange	Button A		GPIO25	9		30	GPIO18		Encoder SPI CLK	Purple	11
12	Brown	Button B		GPIO26	10		29	GPIO05		Encoder SPI CS	Blue	12
13	???	Button C		GPIO27	11		28	GPIO17		Encoder I	Green	13
14	Purple		Switch: Mot Forward	GPIO14	12		27	GPIO16		Encoder A	Yellow	14
15	Grey		Switch: Mot Backward	GPIO12	13		26	GPIO04		Encoder B	Orange	15
16	Black	UI GND	Switch GND	GND	14		25	GPIO0				16
17	White		Switch: Safe Mode	GPIO13	15		24	GPIO02		LED PWM OUT		17
18				X	16		23	GPIO15	jumper			18
19				X	17		22	X				19
20				X	18		21	X				20
21		Diode + jumper to Motor 6V BEC		V IN	19	USB	20	X				21

(Grey = Analog IN pins)
Bottom of board: MALE HEADERS
Blue = 15 pin for UI
Green = 4 pin for Eiki Switch
Red = 7 pin for Motor
Yellow = 15 pin for Encoder

Top of board: FEMALE HEADERS
2x Black 19 pin for ESP32
Black 2 pin for LED PWM out