ESP32 16mm Projector Pinout

Maybe move to GPIO15
due to boot toggle?
        UI Controls
Mot
Mot
Red / Selector Sw / Encoder / Enc	(jump to PCB 3.3v bus)	3.3V	1		38	GND	(Jump to PCB GND bus)
		EN	2		37	GPIO23	Sensor SPI MOSI	White
White	Pot: Shutter Angle	GPIO36	3		36	GPIO22	Motor PWM OUT	Orange
Grey	Pot: Shutter Blades	GPIO39	4		35	X
Purple / Mot	Pot: Lamp Slewing	GPIO34	5		34	X
Blue	Pot: Lamp Brightness	GPIO35	6		33	GPIO21	ESC PGM (+10k pullup)	Yellow
Green	Pot: Motor Slewing	GPIO32	7		32	GND	Sensor Gnd	Black
Yellow	Pot: Motor Speed	GPIO33	8		31	GPIO19	Sensor SPI MISO	Grey
Orange	Button B: Single Backward	GPIO25	9		30	GPIO18	Sensor SPI CLK	Purple
Brown	Button A: Single Forward	GPIO26	10		29	GPIO05	Sensor SPI CS	Blue
Purple	Switch: Mot Forward	GPIO27	11		28	GPIO17	Sensor I	Green
Grey	Switch: Mot Backward	GPIO14	12		27	GPIO16	Sensor A	Yellow
White	Switch: Safe Mode	GPIO12	13		26	GPIO04	Sensor B	Orange
Black	Switch Gnd	GND	14		25	GPIO0
		GPIO13	15		24	GPIO02	LED PWM OUT
		X	16		23	GPIO15
		X	17		22	X
		X	18		21	X
	Motor “BEC” (6V) via diode	V IN	19	USB	20	X

Yellow = Analog IN